## Slide 1: Full circuit, now with TIA
Main driver
Replica driver
Transimpedance amplifier
Channel

## Slide 2: Result: TIA output == inbound data as expected
Paper
Hybrid output
Outbound data
Inbound data
TIA output
My results

## Slide 3: Explanation
In both the paper and my simulation, the TIA input signal is 100 mV peak-to-peak
In the paper, the TIA had an open-loop gain of 5, so my output peak-to-peak swing of roughly 400-500 mV makes sense
Paper: Rf=1.2k
Mine: Rf=6k

## Slide 4: Extension to PAM3
CMOS-inverter-based drivers are no longer suitable
I used the PAM3 output driver from this paper:
  H. Park, J. Song, J. Sim, Y. Choi, J. Choi, J. Yoo, and C. Kim, “30-Gb/s 1.11-pJ/bit single-ended PAM-3 transceiver for high-speed memory links,” IEEE Journal of Solid-State Circuits, vol. 56, no. 2, pp. 581–590, 2020.
I kept the main driver and replica driver output resistance the same, so the other resistances need not change
  Rdrv = 55, Rrep = 275

## Slide 5: PAM3 output driver operation (from the paper)

## Slide 6: Full circuit
Main driver
Replica driver
H
L
!H
!L

## Slide 7: My PAM3 driver output signal with 300mV peak-to-peak swing (same as the paper)

## Slide 8: Full transceiver function with PAM3: hybrid output matches inbound data, as desired, but with significant distortion
Outbound data
Hybrid output
Inbound data

## Slide 9: Post-cursor ISI
Outbound data
Hybrid output
Inbound data

## Slide 10: 1-tap TX Feed-Forward Equalization (FFE)
TX FIR equalization should boost high frequency sections during bit transitions
Should help with migration from NRZ to PAM3 by reducing impact of ISI

## Slide 11: Graph with TX FIR equalization
Outbound data
Hybrid output
Inbound data

## Slide 12: Graph with TX FIR equalization
Outbound data
Hybrid output
Inbound data

## Slide 13
Outbound data
Hybrid output
Inbound data
Outbound data
Hybrid output
Inbound data
Before Tx equalization
Slightly improved level separation
After Tx equalization

## Slide 14
30-Gb/s 1.11-pJ/bit Single-Ended PAM-3 Transceiver for High-Speed Memory Links (JSSC 2021)
Driver
Equalization
  Tx: N/A
  Rx: DFE + CTLE
A 0.275pJ/b 42Gb/s/pin Clock-Referenced PAM3 Transceiver Tolerant to Supply Noise, Reference Offset and Crosstalk for Chiplets and Short-Reach Memory Interfaces (ISSCC 2025)
Clock-referenced PAM3
  Transmitter: a_k = {-A, 0, A}
    D(t) = a_k + n(t)
    CLK_p(t) = +A + n(t)
    CLK_n(t) = -A + n(t)
  Receiver: n(t) gets cancelled
    y_p(t) = D(t) – CLK_p(t) = a_k - A
    y_n(t) = D(t) – CLK_n(t) = a_k + A
Driver
Equalization
  Tx: capacitive-peaking + implicit equalization from FS-puller
  Rx: DFE

## Slide 15: ISSCC 2025 paper
Promises
  Noise cancellation
  Reduced static current, power consumption
Drawbacks
  Nonlinear source
    Mid-level impedance control
PAM 2.5, PAM4