## Slide 1: Nvidia paper LTSpice Simulation
Satvick Acharya

## Slide 2
Component | LTSpice implementation
Main driver | 2-transistor CMOS inverter
Replica driver | 2-transistor CMOS inverter
Rx TIA | 2-transistor CMOS inverter with feedback resistor
Transmission line | LTSpice “tline”
5 nm transistors | From ChatGPT: .model M1 nmos level=54 version=4.7 tox=1.0n nch=1 u0=250 vsat=1.2e7 vth0=0.35 + rdsw=100 vdsat=0.1 cox=3e-2 cgso=1e-10 cgdo=1e-10 .model M17 pmos level=54 version=4.7 tox=1.0n nch=1 u0=90 vsat=1.0e7 vth0=-0.35 + rdsw=100 vdsat=0.1 cox=3e-2 cgso=1e-10 cgdo=1e-10
Main driver

## Slide 3
Main driver
Replica driver
Channel
TIA

## Slide 4
Main driver
Replica driver
Channel
TIA

## Slide 5
Vdrv
Vrep
Vout
Vdata

## Slide 6: Vdata_a = Vout_b and Vdata_b = Vout_a

## Slide 7: Vdrv_a is a flipped version of Vrep_a

## Slide 8: Deviations from paper / limitations of my simulation
Main and replica driver topology is different in the paper
I used a 1 ps delay transmission line with no timing/synchronization circuitry
I will need to implement this eventually
Extra shunt capacitance at replica driver output
I added this later, because without it, I was unable to achieve Vout_a = Vdata_b or Vout_b = Vdata_a
It helped me achieve Vdrv = Vrep by mimicking the loading effect of the channel

## Slide 9: My questions
How can I better model this driver circuit?
I am unsure what the “slices” are referring to as I don’t think it was referenced anywhere else in the paper.
My understanding is that circuits are needed at the replica driver output (like the shunt capacitance I used). What kinds of circuits are commonly used and how does each component impact the shaping of the replica signal?

## Slide 10: Using the exact same circuit but with PAM3 input signals
I’m going to start experimenting with approaches to improve this result